## Slide 1: Welcome to HeatSync Labs!
We are a 501(c)3 non-profit, we have no employees
Entirely volunteer run
Our goal is to create a space where the public can create things!
For more information about the space and what goes on here, please visit http://www.heatsynclabs.org

## Slide 2: Mechanical Assembly

## Slide 3: Inventory
13 M3x25
1
M3x30
1x metal
1x nylon
M4
Pen Holder
¾” x ½” Spring
M8x60
2x
Bearing Mount
2x
Skateboard
Bearings
22x
M8 Nut
M4 Washer
6x
M3 Nut
(1 with silvered side)
Egg Holder
Drive
Egg Holder
Idler
2x
NEMA 17
Steppe Motors
Arduino Holder
Pen Axis Plate
2x
Egg Axis Plate
2x
Table Rest
Drive Brace
Idler Brace
Pen Arm Shaft Coupler
Pen Arm
Distal
Pen Arm Proximal
3x
M8 Threaded Rod
2 nylon
1 metal
M4 Nut
Ⓓ
Ⓖ
Ⓚ
Ⓗ
Ⓘ
Ⓙ
Ⓝ
Ⓥ
Ⓤ
Ⓞ
Ⓜ
Ⓒ
Ⓑ
Ⓔ
Ⓕ
Ⓦ
ⒶⒷⒸⒹⒺⒻⒼⒽⒾⒿⓀⓁⓂⓃⓄⓅⓆⓇⓈⓉⓊⓋⓌⓍⓎ①②③④⑤⑥⑦⑧⑨⑩
Ⓛ
Ⓠ
Ⓟ
Ⓢ
Ⓣ
Ⓧ
Ⓡ
Ⓨ
Ⓐ
M8 Washer
Ⓩ
2x
Dart Tips
①
9g Servo
②
4
M3 Standoff
③

## Slide 4: Final Assembly

## Slide 5: STEP 1
Ⓓ
Ⓘ
3xⓅ
Ⓨ
M4 Bolt – nylon (shorter)
M4 Nut - Metal
Press in nuts using clamp
Push coupler onto shaft against table
Motor shaft should be flush
Note: Nuts do not go flush

## Slide 6: STEP 2
Ⓤ
4xⒼ
Trim nylon screws using 1 green spacer + 1 purple spacer

## Slide 7: STEP 3
Ⓖ
Ⓢ
Ⓙ
Ⓔ
Ⓕ
This M3 nut has a SILVER side that must face up!

## Slide 8: STEP 4
Ⓠ
Ⓘ
M4 nut, metal
Use one of the two long screws that comes in the servo bag to attach
③

## Slide 9: STEP 5 (center onto rods)
Ⓐ
Ⓐ
Ⓡ
Ⓡ
Ⓡ
Ⓡ

## Slide 10: STEP 6
Ⓧ
3xⒼ
Ⓚ
Ⓝ
Ⓞ
Ⓞ
Ⓝ
3xⓈ
Ⓥ
Ⓛ
Ⓩ
①
Update: The head screws off of the new version and installs from the left!

## Slide 11: STEP 7
Ⓡ
Ⓡ
Ⓡ
Ⓡ
Ⓡ
Ⓡ
Ⓡ
Ⓡ
Ⓜ
Ⓗ
Ⓢ
Ⓒ

## Slide 12: STEP 8
Ⓓ
Ⓥ
3xⒼ
Ⓣ
①
Trim these bolts!
use 1 green spacer + 1 purple spacer

## Slide 13: STEP 9
Ⓡ
Ⓡ
Ⓡ
Ⓡ
Ⓡ
Ⓡ
Ⓡ
Ⓡ
Ⓜ
Ⓖ
Trim this bolt! use 2 green spacers
Ⓑ

## Slide 14: STEP 10
Ⓦ
②
②
②
②

## Slide 15: Electrical Assembly

## Slide 16: Electronic Inventory

## Slide 17: Controller Anatomy
Egg
Axis
Connector
Pen
Axis
Connector
Spare
(For future world domination?)
A4988 Stepper Motor Drivers
Arduino Nano
USB to Computer (Data port)
12V power 
Pen arm lifter upper Servo

## Slide 18: Hack the Mainboard Pt I
There is a mistake on the board. These four pins MUST be connected together!
Remove all the green jumpers from these three areas. They must be all gone, like this!
Solder them together, like this. Do this for all three sets.

## Slide 19: Hack the Mainboard Pt II
This is the reset pin. We need to keep it from resetting every time we connect to the board. To do this, we will add a capacitor.
This is a capacitor. It has a front, and a back. The positive, + side is marked with a darker stripe. Yes, it is tiny!
+

## Slide 20: Hack the Mainboard Pt II
Place the capacitor sideways next to the reset pin pair. Gently touch each leg with the soldering iron on the FAR side of the capacitor.
Pay careful attention to the dark stripe, it must be facing the right way!
Heat from THIS side
Done!

## Slide 21: Stepper Motor Drivers
These tiny boards are called drivers, because they control the motors.
They need to be adjusted for the motors we are using.
The formula is Voltage = Amps * 0.8
Our motors need 0.35 Amps, which means 0.35*0.8 = 0.28 Volts
Insert the drivers into the main board, like this. Pay attention! If you plug them in backwards you will fry them!
Measure here
Here’s another
view
Have a friend turn the dial while you measure with a meter!
And here

## Slide 22: Program your Arduino
Remember when we soldered that capacitor? It keeps the Arduino from resetting, which means we can’t program it when its plugged in.
To program the Arduino, first install the file in the Step-1 folder on the thumb drive.
  Plug in your Arduino to the blue cord, then to your PC
  Open the subfolder EggDuinoNanoJN and run ‘EggDuinoNanoJN.ino’
  This will launch the Arduino IDE, wait for it to pop up
  Run Sketch->Upload to program the Arduino. Unplug when done and close Arduino

## Slide 23: Insert your Arduino and hook it all up!
Be careful not to get it backwards!
 The USB is here
The servo goes on these three pins. Brown must be hooked to the pin labeled GND
The stepper motor wires go green to the LEFT as shown here

## Slide 24: Power it up!
It’s go time! But before we apply power, have an instructor do a once-over to make sure everything is as it should be to avoid damaging anything.
Ok? OK! Plug the 12V power adapter into a wall outlet then into the controller board.
If you did everything right, both stepper motors and the servo should come ALIVE for about a second, then relax.
If either nothing happens OR something horrible happens, remove power IMMEDIATELY and ask for assistance (DON’T PANIC!) 

## Slide 25: Add Servo Horn
Servos are motors that move through small carefully controlled range
  They do not make a full circle, usually 180 Degrees, a half circle.
  When we powered on the device, the stepper was commanded to its home position.
  Now we can add the last piece, the horn.
Press the horn onto the shaft so that it just touches the plastic but does not lift it up.
It is better to have a small gap than to push the arm up.
Secure with the SMALL screw from the servo baggie.
Servo Horn

## Slide 26: Pen Holder
Servos are motors that move through small carefully controlled range
  They do not make a full circle, usually 180 Degrees, a half circle.
  When we powered on the device, the stepper was commanded to its home position.
  Now we can add the last piece, the horn.
Press the horn onto the shaft so that it just touches the plastic but does not lift it up.
It is better to have a small gap than to push the arm up.
Secure with the SMALL screw from the servo baggie.
Servo Horn

## Slide 27: Software Setup

## Slide 28: Install Inkscape
Run the files located in the step-2 directory on the thumbdrive
  This will install inkscape and the eggbot extensions from Evil Mad Scientist
Run Inkscape, and open the Eggbot Extension

## Slide 29: Setup EggBot Control
The following screens show the settings for use on your robot.
Keep this as a reference

## Slide 30: Forward!
Visit http://wiki.evilmadscientist.com/The_Eggbot_Extensions for a wonderfully written tutorial on how to use Inkscape to generate art!